## Slide 1
Types of Networks

## Slide 2
1. Types of Networks
Personal Area Networks (PANs):
  Purpose: Connect personal devices (e.g., mobile phones, tablets, cameras).
  Wireless PANs (WPANs): Increasingly important (e.g., Bluetooth).
  Range: 10–30 meters.
  Bandwidth: 0.5–2 Mbps.
  Latency: 5–20 ms.

## Slide 3
1. Types of Networks
Local Area Networks (LANs):
  Purpose: High-speed communication within a limited area (e.g., office, campus).
  Technologies: Ethernet (dominant), token rings, slotted rings.
  Range: 1–2 km.
  Bandwidth: 10 Mbps–10 Gbps.
  Latency: 1–10 ms.

## Slide 4
1. Types of Networks
Metropolitan Area Networks (MANs):
  Purpose: High-bandwidth communication within a city.
  Technologies: Ethernet, ATM, DSL, cable modems.
  Range: 2–50 km.
  Bandwidth: 1–600 Mbps.
  Latency: 10 ms.

## Slide 5
1. Types of Networks
Wireless Networks:
  WLAN (WiFi, IEEE 802.11):
    Range: 0.15–1.5 km.
    Bandwidth: 11–108 Mbps.
    Latency: 5–20 ms.
  WMAN (WiMAX, IEEE 802.16):
    Range: 5–50 km.
    Bandwidth: 1.5–20 Mbps.
    Latency: 5–20 ms.

## Slide 6
1. Types of Networks
Wireless Networks:
  WWAN (3G/4G Mobile Networks):
    Range: 1-5 KM (cell-based)
    Bandwidth: 348 kbps-14.4 Mbps(3G), up to 100 Mbps (4G).
    Latency: 100-500 ms.

## Slide 7
2. Internetworks
Definition: Integration of multiple networks into a single communication subsystem.
Purpose: Enable extensible, open distributed systems.
Components:
  Routers: Dedicated switching computers.
  Gateways: General-purpose computers.
Example: The Internet (TCP/IP protocols).

## Slide 8
3. Key Characteristics
Performance:
  Latency: Delay in message transmission.
  Bandwidth: Data transfer rate
  System Bandwidth: Total throughput of the network.
Scalability: Ability to handle growth in size and load.
Reliability: High in wired networks; lower in wireless due to interference.
Errors:
  Packet Loss: Due to buffer overflow or processing delays.
  Out-of-Order Delivery: Common in WANs.
  Duplicate Packets: Caused by retransmissions.

## Slide 9
4. Ethernet (LAN Technology)
Dominance: Most widely used LAN technology.
Evolution:
  10 Mbps (Original)
  100 Mbps, 1 Gbps, 10 Gbps (Modern versions)
Switching Mode: Improves performance for multimedia applications.

## Slide 10
5. Wireless Networks
WiFi (IEEE 802.11):
  Widely used for mobile devices and home/office networks.
WiMAX (IEEE 802.16):
  Alternative to wired MANs.
3G/4G Mobile Networks:
  Provide wide-area mobile Internet access.
  3G: 2–14.4 Mbps.
  4G: Up to 100 Mbps.

## Slide 11
6. DSL and Cable Modems
DSL:
  Uses existing telephone lines.
  Speeds: 1-10 Mbps
  Range: Up to 5.5 Km.
Cable Modems:
  Uses coaxial cable (TV networks)
  Speeds: Up to 15 Mbps
  Greater range than DSL

## Slide 12
7. Key Takeaways
Network Types:
  PANs, LANs, WANs, MANs, and wireless variants serve different needs.
Performance:
  Latency and bandwidth vary significantly across network types.
Internetworks:
  Combine multiple networks for scalable, open communication.
Ethernet:
  Dominates wired LANs; evolved to support high-speed applications.
Wireless Networks:
  Enable mobility and flexibility but face challenges like interference.
Errors:
  Packet loss, out-of-order delivery, and duplicates are common in WANs.