## Slide 1
PROTECTION

## Slide 2
1. Types of illegitimate access to resources
Malicious or buggy code: Not only hostile code but also “benign” code with bugs can jeopardize system integrity.
Example – File with two operations (read, write):
  Access rights: Smith can read/write, Jones can only read. If Jones manages to write, that’s a form of illegitimate access.
  Sidestepping exported operations: Invoking unexposed operations (e.g., setFilePointerRandomly) is also illegitimate.

## Slide 3
2. Protection at the language level
Type-safe languages (e.g., Sing#, Modula-3) restrict access to modules via references only.
  If you don’t have a valid reference, you cannot invoke or manipulate the module.
  Arbitrary pointer operations (possible in C/C++) are disallowed or significantly restricted.

## Slide 4
3. Hardware-level protection with kernels
Kernel characteristics:
  Remains loaded from system initialization with full (supervisor) access to hardware resources.
  Manages the memory management unit (MMU) and CPU registers to ensure no illicit resource usage by processes.
Supervisor mode vs. user mode:
  Most CPUs have a mode register (privileged/unprivileged).
  Kernel code runs in supervisor mode (privileged instructions allowed).
  User processes run in user mode (restricted instructions).

## Slide 5
4. Address spaces
The kernel sets up address spaces to protect itself and other processes.
  Each address space has specific read/write/execute privileges.
  A process cannot access memory outside its assigned address space.
User processes: Operate with user-level address spaces (restricted).
Kernel operations: Execute within the kernel’s address space (full privileges).

## Slide 6
5. System calls and traps
Transition between user space and kernel space happens via special CPU exceptions (interrupts or system call traps).
A system call trap instruction (e.g., TRAP) switches the processor to supervisor mode and jumps to a kernel handler function.
This prevents user-level processes from directly manipulating hardware settings.

## Slide 7
6. Performance Trade-off
Protection incurs overhead:
  Switching address spaces costs many CPU cycles.
  A system call trap is more expensive than a simple procedure call.
Designers must balance security and performance when building OS and middleware services.